## Slide 1
Chapter 2
Network Models
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
2-1 LAYERED TASKS
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.
Sender, Receiver, and Carrier Hierarchy
Topics discussed in this section:

## Slide 3
Figure 2.1 Tasks involved in sending a letter

## Slide 4
2-2 THE OSI MODEL
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
Layered Architecture Peer-to-Peer Processes
Encapsulation
Topics discussed in this section:

## Slide 5
ISO is the organization. OSI is the model.
Note

## Slide 6
Figure 2.2 Seven layers of the OSI model

## Slide 7
Figure 2.3 The interaction between layers in the OSI model

## Slide 8
Figure 2.4 An exchange using the OSI model

## Slide 9
2-3 LAYERS IN THE OSI MODEL
In this section we briefly describe the functions of each layer in the OSI model.
Physical Layer Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
Topics discussed in this section:

## Slide 10
Figure 2.5 Physical layer

## Slide 11
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.
Note

## Slide 12
Figure 2.6 Data link layer

## Slide 13
The data link layer is responsible for moving frames from one hop (node) to the next.
Note

## Slide 14
Figure 2.7 Hop-to-hop delivery

## Slide 15
Figure 2.8 Network layer

## Slide 16
The network layer is responsible for the delivery of individual packets from
the source host to the destination host.
Note

## Slide 17
Figure 2.9 Source-to-destination delivery

## Slide 18
Figure 2.10 Transport layer

## Slide 19
The transport layer is responsible for the delivery of a message from one process to another.
Note

## Slide 20
Figure 2.11 Reliable process-to-process delivery of a message

## Slide 21
Figure 2.12 Session layer

## Slide 22
The session layer is responsible for dialog control and synchronization.
Note

## Slide 23
Figure 2.13 Presentation layer

## Slide 24
The presentation layer is responsible for translation, compression, and encryption.
Note

## Slide 25
Figure 2.14 Application layer

## Slide 26
The application layer is responsible for providing services to the user.
Note

## Slide 27
Figure 2.15 Summary of layers

## Slide 28
2-4 TCP/IP PROTOCOL SUITE
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model. The original TCP/IP protocol suite was defined as having four layers: host-to-network, internet, transport, and application. However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.
Physical and Data Link Layers Network Layer Transport Layer
Application Layer
Topics discussed in this section:

## Slide 29
Figure 2.16 TCP/IP and OSI model

## Slide 30
2-5 ADDRESSING
Four levels of addresses are used in an internet employing the TCP/IP protocols: physical, logical, port, and specific.
Physical Addresses Logical Addresses Port Addresses Specific Addresses
Topics discussed in this section:

## Slide 31
Figure 2.17 Addresses in TCP/IP

## Slide 32
Figure 2.18 Relationship of layers and addresses in TCP/IP

## Slide 33
In Figure 2.19 a node with physical address 10 sends a frame to a node with physical address 87. The two nodes are connected by a link (bus topology LAN). As the figure shows, the computer with physical address 10 is the sender, and the computer with physical address 87 is the receiver.
Example 2.1

## Slide 34
Figure 2.19 Physical addresses

## Slide 35
As we will see in Chapter 13, most local-area networks use a 48-bit (6-byte) physical address written as 12 hexadecimal digits; every byte (2 hexadecimal digits) is separated by a colon, as shown below:
Example 2.2
07:01:02:01:2C:4B
A 6-byte (12 hexadecimal digits) physical address.

## Slide 36
Figure 2.20 shows a part of an internet with two routers connecting three LANs. Each device (computer or router) has a pair of addresses (logical and physical) for each connection. In this case, each computer is connected to only one link and therefore has only one pair of addresses. Each router, however, is connected to three networks (only two are shown in the figure). So each router has three pairs of addresses, one for each connection.
Example 2.3

## Slide 37
Figure 2.20 IP addresses

## Slide 38
Figure 2.21 shows two computers communicating via the Internet. The sending computer is running three processes at this time with port addresses a, b, and c. The receiving computer is running two processes at this time with port addresses j and k. Process a in the sending computer needs to communicate with process j in the receiving computer. Note that although physical addresses change from hop to hop, logical and port addresses remain the same from the source to destination.
Example 2.4

## Slide 39
Figure 2.21 Port addresses

## Slide 40
The physical addresses will change from hop to hop,
but the logical addresses usually remain the same.
Note

## Slide 41
Example 2.5
As we will see in Chapter 23, a port address is a 16-bit address represented by one decimal number as shown.
753
A 16-bit port address represented as one single number.

## Slide 42
The physical addresses change from hop to hop,
but the logical and port addresses usually remain the same.
Note